## Slide 1: RipStream: Testing effects of management strategies on stream temperature
Jeremy Groom
Oregon Department of Forestry

## Slide 2: RipStream – Riparian Function and Stream Temperature
State and Private Forests joint effort
Objective: Evaluate effectiveness of forest practices rules & strategies at protecting stream temperature, promoting riparian structure
33 Sites (18 Private, 15 State, Medium and Small F)

## Slide 3: Rules and Strategies
Private: Forest Practices Act
State: Northwest Oregon State Forest Management Plan
State Forests
Private Forests
170 ft
25 ft
20 ft
50 ft
70 ft
Limited Entry
No
Cut
No
Cut
Limited
Entry (1)
Small & Medium F
Small F
Medium F
100 ft
Limited
Entry (2)

## Slide 4: RipStream Study Design
Design: 2 years pre-harvest, 5 years post harvest
1W
Control
Treatment
2W
3W
4W

## Slide 5: Study Management Differences
Numbers of sides harvested:
  State: 13 = 1 side, 2 = 2 sides
  Private: 4 = 1 side, 14 = 2 sides
Harvest types:
  State: 7 sites partial-cut (thin), 8 sites clearcut
  Private: All 18 sites clearcut

## Slide 6: RipStream – Data and Questions
Questions:
How did temperatures change immediately post-harvest? 5 yrs post-harvest?
Years of data collection
  Stream temperature
  Shade
  Channel morphology (gradient, widths, etc.)
  Riparian vegetation
  (trees, shrubs)

## Slide 7: Regulatory Analysis: DEQ Water Temperature Standards
Biologically-Based Numeric Criteria – were stream temperatures raised above 16 C or 18 C?
  No
  Analysis: Relatively straightforward
Protecting Cold Water (PCW) – were streams warmed by > 0.3 C?
  Yes, on private (not State) streams
  Analysis: Complex

## Slide 8: Numeric Criteria Results: 16 & 18 C
Total Number of Sites: 33
Twelve 18 C sites
Twenty-one 16 C sites
Seven sites exceeded threshold at 3W
  3 sites = control (1W, 2W) and treatment (3W) probes exceeded during the same year or years
  1 site = treatment probe pre-harvest and post-harvest
  1 site = control probes during pre-harvest years; treatment probes during post-harvest year(s)
  2 sites = treatment probe post-harvest only
 No strong indication that standards exceeded

## Slide 9: Study Design and the PCW
3 reaches X 3 time periods = 9 groups
Pre-pre Pre-post Post-post
Upstream
Control
Treatment
Downstream
1W
4W
2W
3W
FLOW
614 comparisons total
65 exceedances
Pre 1
Pre 2
Post 2
Post 1

## Slide 10: Protecting Cold Water
40.2%
4.6%
Water Resources Research 2011

## Slide 11: Findings so far: 2 years postharvest
Effects analysis:
To what degree did temperatures change? Why?
Private sites: temperature increased + 0.7 °C (2.5, -0.9)
State sites: + 0.0 °C (1.0, -0.9)
Temperature increases
related to declines in shade
Shade related to riparian
basal area (+), tree height (-)
Forest Ecology and
Management (2011)

## Slide 12: Change in Shade Pre- to Post-harvest
Pre-harvest
Post-harvest

## Slide 13: State Forest Sites
Factors relating to State temperature changes:
  Treatment reach length (+)
  Control reach Δtemperature (NS)
  Postharvest Clearcut (-)*
Shade did not differ greatly between years
Not much change in basal area within 53m
Negative temperature change with clear-cut?

## Slide 14: Max Temperature: Post-1 thru Post-5 Preliminary findings
Variable: Pre-Post difference = change pre-harvest to post-1.
Response: Δtreatment temperature
Predictors:
Treatment reach length (+)
Control temp change (-)
Pre-Post difference (+)
Years Postharvest (-)
Pre-Post*Years interaction (-)
Opposite, similar model for shade
Site 5559

## Slide 15: Summary
Initial response:
  Private sites = temperature increase, shade decrease
  State sites = no signal
      RMA basal area, shade relatively unchanged
      Clear-cuts beyond RMA ≠ temperature increase
  Shade related to basal area, height
5-year response:
  Similar important factors
  Temperature: initial increase followed by decrease
  Shade: initial decrease followed by increase
Next:
  Downstream temperatures
  Wood recruitment

## Slide 16: Acknowledgements
Private Forest monitoring staff (Marganne Allen, Jerry Clinton, Kevin Nelson, Kyle Abraham, John Hawksworth, Seasonal Work Force, Stewardship Foresters)
Private landowners
State Forests Program Staff (Liz Dent, Jeff Brandt, District Foresters, Field Foresters)
Review Committee Members
EPA/DEQ 319 program
Headwaters Research Cooperative

## Slide 18: Buffer width & minimum FPA
Stated results (Groom et al. 2011b):
But a small F buffer for private = 50 ft (15 m) max!
… “harvested to minimum FPA”??
Variable | State- mean | State- range | Private- mean | Private- range
Buffer Width (m) | 51.8 | 25-61 | 31 | 19-41

## Slide 19
Mean vs. Median
>200’
>200’
50’
50’
25’
Mean w/
>200’ = 105’
Mean w/o
>200’ = 42’
Median = 50’
2W
3W
RMA
Buffer width & minimum FPA

## Slide 20: Buffer width & minimum FPA
Could have left out 2W & 3W buffer measures
5204 (Ice Box: 107’ to 56’)
5503 (Siletz Creek) – strong meander, alders
Summary:
  We rigorously followed protocol
  Buffer width can be a nasty thing to quantify…
  Medians would have been better
  Even better yet, begin measurements 50’ or 100’ away from probe, more measurements.