## Slide 1
LiDAR-based assessment of sunlight distribution in forest ecosystems
Demetrios Gatziolis
USDA Forest Service
PNW Research Station
dgatziolis@fs.fed.us
http://pnwfia.info/dgatziolis
April 23, 2015
Notes: By using precisely georeferenced and timed observations of direct sun illumination conditions, I managed to determine the accuracy of this approach in the Malheur NF. Please note that precise georeference, one foot or better, is a prerequisite for an unbiased assessment thanks to the high spatial variability of light mentioned earlier. Obtaining such georeferencing precision levels is a difficult and costly operation, especially in the western Cascades and the coastal mountains. As you can see, the fit is very good especially if the two outliers are removed. The first of the two points farther away from the red 1:1 line corresponds to a location where a defoliator appeared in the one growing season between LiDAR acquisition and field measurements. The second was near a stand profile exposed by thinning that occurred shortly before we went to the field.
Next slide please.

## Slide 2
Motivation
  Diurnal and seasonal distribution of sunlight
  Influences tree growth, regeneration potential, wildlife habitat, stream temperature, and various other ecological processes
Difficult to assess precisely and without bias
Has management and policy implications
Proliferation of publicly available, high-density LiDAR data
90+% of Oregon forests scanned at least once
Potential for inexpensive, small area acquisitions (UAVs)

## Slide 3
Current methods for assessing sunlight distribution
  Developed for applications using bare earth representations
  Degenerate 3D vegetation and terrain data into 2.5D
  Consider trees opaque objects
  Under canopy ground and lateral crown illumination are not defined
  Incompatible with needs to determine which scene element(s) is responsible for shade on a particular location
  Strongly biased (shade overestimation)

## Slide 4
Elements of LiDAR technology
Volumetric pulse – object interaction

## Slide 5
From point clouds to voxel space representation

## Slide 6
Ray tracing in voxel space
  Determine voxel resolution
  Generate voxel representation
  Calculate ray azimuth and elevation angle
  Compute the ray’s ‘voxel walk’
  Stop if the ray intersects a ‘filled’ voxel
  The process is computationally intensive and demanding of computer hardware resources (memory)
  Efficient execution requires series of optimizations and execution in parallel (multithreading)

## Slide 7
Point cloud to voxel space representation
to light assessment via ray tracing

## Slide 8
Prediction accuracy
  N = 52
  RMSD = 0.145 (7.25%)
  R2 = 0.92
  If outliers are excluded:
  N = 50
  RMSD = 0.053 (2.65%)
  R2 = 0.98
Notes: By using precisely georeferenced and timed observations of direct sun illumination conditions, I managed to determine the accuracy of this approach in the Malheur NF. Please note that precise georeference, one foot or better, is a prerequisite for an unbiased assessment thanks to the high spatial variability of light mentioned earlier. Obtaining such georeferencing precision levels is a difficult and costly operation, especially in the western Cascades and the coastal mountains. As you can see, the fit is very good especially if the two outliers are removed. The first of the two points farther away from the red 1:1 line corresponds to a location where a defoliator appeared in the one growing season between LiDAR acquisition and field measurements. The second was near a stand profile exposed by thinning that occurred shortly before we went to the field.
Next slide please.

## Slide 9
Application capabilities
  Shade/light assessment possible anywhere high-density LiDAR data are available
  User can specify time span, over the day and year, and number of solar positions to be considered during processing
  Generate illumination/shade summaries in tabular or georeferenced raster format
  Assess shade/light regimes at ground surface, at any point or level in the canopy, or at a constant above-ground offset
  Restrict computations within an AOI

## Slide 10
Application capabilities (cont.)
  3D visualizations of scene illumination conditions for a sequence of sun locations that can be assembled as an animation
  Simulate the impact on shading of management activities such as harvest, relative to no-action alternatives
  Delineate variable width buffers around stream reaches outside of which harvest won’t reduce shading by more than a specified threshold

## Slide 11
Direct illumination
of ground
Direct illumination
of ground and vegetation
Rays cast
5am : 8pm
@ 12 min intervals

## Slide 12
  Percent direct solar illumination of ground surfaces
  25 ft resolution
  6 days, 20 rays / day
  2007 LiDAR acquisition
  4,133 billion laser returns
  Distribution moments:
  Min: 0.0%
  Mean: 19.8%
  Max: 100.0%
  SD: 19.4%
  Stream layer from R. Hassmiller
Mainstem CampLick, Malheur NF

## Slide 13
Shade management with variable-width harvesting buffer around a stream reach

## Slide 14
Dynamic assessment of shade/sunlight in forest ecosystems using high-density LiDAR data
Demetrios Gatziolis
USDA Forest Service
PNW Research Station
dgatziolis@fs.fed.us
http://pnwfia.info/dgatziolis
April 23, 2015
Notes: By using precisely georeferenced and timed observations of direct sun illumination conditions, I managed to determine the accuracy of this approach in the Malheur NF. Please note that precise georeference, one foot or better, is a prerequisite for an unbiased assessment thanks to the high spatial variability of light mentioned earlier. Obtaining such georeferencing precision levels is a difficult and costly operation, especially in the western Cascades and the coastal mountains. As you can see, the fit is very good especially if the two outliers are removed. The first of the two points farther away from the red 1:1 line corresponds to a location where a defoliator appeared in the one growing season between LiDAR acquisition and field measurements. The second was near a stand profile exposed by thinning that occurred shortly before we went to the field.
Next slide please.