## Slide 2
Rogue
Valley
LiDAR
Derived
Stand
Metrics

## Slide 3
Rogue Valley LiDAR
Mid Rogue River, South Roseburg, Rock Cr,
Upper Coquille
Flown in 2012
~1.4 Million Acres
~650K BLM/ODF

## Slide 4
LiDAR Source Reference Material
Rogue Valley BLM Stratified LIDAR
Sample Plot Methodology, March, 2013
Rogue Valley LIDAR Inventory
Plot Establishment, February 24, 2014
Notes: LiDAR Source Reference Material
The details are in reference documents. Cheryl Friesen made copies.

## Slide 5
Components to
Derive Stand Metrics
LiDAR Bins
  Pixelated to 75 Feet
Correlation Plot Tree Data
BLM FOI-VEG
Classified Forest Stands

## Slide 6
Principle Components Analysis
Bin Development by Significance
1st Component
80TH Percentile Height
  80% of LiDAR height returns below this point.
  Six fixed width (30 ft) classes
  Highly accurate for height prediction.
Cover %
  Three equal-width density classes
  Low (1), Moderate (2), High (3)

## Slide 7
18 Bins (Strata)

## Slide 8
18 Bins (Strata)
Notes: For the bins
[click] the first number represents the height classes. As you can see there are six.
[click] the second number represents the percent cover classes represented by 1-3 or Low, Mod, High.
Combined it gives a total of 18 bins.

## Slide 9
Bin Statistics

## Slide 10
Correlation Plots
Primary
Plots
(blue)
Alternate
Plots
(red)

## Slide 11
Correlation Plot Tree Data
2ND Component
240 Plots
~13 Plots per Bin
Tree List Generated per Bin
Notes: Correlation Plot Data – 2nd Component
Tree lists were generated for each bin from the 13 plots.

## Slide 12
Correlation Plot Data
EcoSurvey Avg Stand Metrics per Bin
Notes: EcoSurvey Avg Stand Metrics per Bin
The tree lists for each bin were run through BLM’s EcoSurvey program (probably similar to FS-VEG) to generate average stand metrics per bin as you see here.
[click] Unfortunately seedling counts were pulled from the correlation plot contract due to budget constraints.
[click] Also notice for these stand averages, I took out the Rock Creek and East Fork Coquille plot data because they are so different from the SW Oregon drier forest stands.

## Slide 13
LiDAR Veg Height Color Blend
Provides Visual Contrast
One Meter Pixels

## Slide 14
LiDAR & BLM FOI-VEG Polygons
3rd Component
BLM
Forest Stand
Polygons
Notes: LiDAR & BLM FOI-VEG Polygons – 3rd Component
The third component involves using BLM’s FOI-VEG forest stand polygons. This picture reflects the checkerboard ownership of BLM lands These provide the backbone of BLM’s forest inventory of like kind forest stands.

## Slide 15
LiDAR & BLM FOI-VEG Polygons
Bin Pixels Intersected with Forest Stand
Notes: LiDAR & BLM FOI-VEG Polygons – 3rd Component
Within each FOI-VEG polygons a weighted average of bins can be developed by intersecting in GIS the FOI-VEG polygons with the bins.

## Slide 16
LiDAR & BLM FOI-VEG Polygons
Bin Weighted Avg per Forest Stand
Notes: LiDAR & BLM FOI-VEG Polygons
Once intersected the number of pixels per bin and total number of intersected pixels per FOI-VEG polygon is given as shown in this partial spreadsheet.

## Slide 17
LiDAR & BLM FOI-VEG Polygons
Bin Weighted Avg per Forest Stand
Notes: LiDAR & BLM FOI-VEG Polygons
Using the number of pixels per bin and total per FOI-VEG forest stand polygon, a weighted average for each bin is calculated as shown in this partial spreadsheet.

## Slide 18
LiDAR Derived Stand Metrics
Weighted Average of the Averages
Notes: LiDAR Derived Stand Metrics
Those weighted averages are then multiplied by the averages for each bin generated tree list and added together for each FOI-VEG forest stand to get the weighted average stand metrics.

## Slide 19
LiDAR Derived Stand Metrics
Does not Give Species Mix,
Only Stand Metrics
Species Already Part of BLM’s Forest
Stand Description
Initial Quick Guide for the Field Forester
Notes: LiDAR Derived Stand Metrics

## Slide 20
Comparisons with Stand Exams
Preliminary comparisons on 80 stands
Inconclusive at this point
Need more testing & refinement

## Slide 21
GIS Tools to Summarize
Stand Metrics by Unit
John Guetterman
GIS Lead Coos Bay BLM

## Slide 22
Summarizing Stand Metrics by Unit

## Slide 23
Summarizing Stand Metrics by Unit
Output = Area-weighted average by polygon
(harvest unit or whatever?)

## Slide 24
Summarizing PNW Stand Metrics by Unit

## Slide 25
Summarizing PNW Stand Metrics by Unit
Output = Area-weighted average by polygon
(harvest unit or whatever?)
 | Area-weighted Averages |  |  |  |  |  |  | 
Unit # | BA | CanopyBaseHt | CrownLen | HtLoreysLive | HtTop40 | QMD | TPA | VolCuft
11 | 168.0 | 49.1 | 42.2 | 87.2 | 97.5 | 14.6 | 192.5 | 6,458
9 | 146.9 | 42.9 | 40.7 | 81.6 | 88.0 | 13.6 | 189.1 | 5,230

## Slide 26
LiDAR
Stand Metrics
QUESTIONS?