## Slide 1: Using LiDAR to Inform NEPA
John Colby – Umpqua Field Office Hydrologist
John Guetterman – GIS Specialist
Coos Bay District BLM

## Slide 2
DEM 10m + BLM Hillshade
Hillshade (bare earth)
TPI 30m + Hillshade (bare earth)

## Slide 3: DOGAMI southern Oregon coast study area
Acquisition: 2008 & 2009
Area of interest: 1.6 million acres covering portions of 4 counties
LiDAR Consortium
  Led by DOGAMI
  CBD BLM 72% coverage or 232,709 acres out of 322,148 total District acres
  Cost $175k CBD + $400k OSO
  Other partners: USFS, BIA, ODF, State, USACE, private

## Slide 4: DOGAMI southern Oregon coast study area
Leaf on
  Average pulse density = 8.10 per m2
  Average ground density = 0.57 per m2
Basic products
  1st return DEM
  Bare earth DEM
Point cloud data available from OSO for specific needs

## Slide 5: Umpqua Field Office NEPA
EA | Harvest acres | Tree age | No. of units
URSR | 8,963 | 31-80 | 104
Fairview | 7,344 | 40-75 | 83
Soup Cr. | 111 | 67 | 2
Big-Vincent | 6,341 | 34-62 | 31
> 70% of in-unit streams 1st & 2nd order

## Slide 6
LiDAR a useful tool
Stream delineation
Stream inception points
Shade duration
LWD source areas

## Slide 7: Stream Delineation

## Slide 8: Stream Network Delineation Workflow
Use surface area rather than planimetric area when calculating upslope contributing area with the D-infinity algorithms
Apply Perona-Malik filtering to smooth surface noise while maintaining edges
Incise DEMs to breach depressions at road crossings and other physical obstructions
Fill all other depressions
Estimate channel initiation points using a combination of local curvature and upslope contributing area
Delineate stream network using least-cost path analysis
1:8,000
Draft watershed boundary and stream network delineation
Courtesy of Craig Ducey, OSO GIS/Remote Sensing Specialist

## Slide 9: Stream Network Delineation Workflow
Prepare data for NHD steward review
Revise stream network by deleting, adding, or moving channel initiation points
Estimate periodicity using Shreve stream order
Apply minimal smoothing to improve line geometry aesthetics
Migrate attribution and update the NHD corporate dataset
Revise watershed boundaries and update the WBD corporate dataset
1:8,000
Final watershed boundary and stream network delineation
Courtesy of Craig Ducey, OSO GIS/Remote Sensing Specialist

## Slide 10: Stream Inception Points - Office
Generate streams with steps from Craig’s earlier work + ESRI tools
Mark inception points
Create paper maps
Load unit boundary and LiDAR streams on GPS

## Slide 11: Stream Inception Points - Field
Many hands make light work
Protection of the resource
National Hydrography Dataset (NHD) revisions

## Slide 12: Perennial buffer widths
Operational considerations
Unstable ground
Shade
LWD source areas
Hardwoods only
Mixed forest
Pronounced inner gorge

## Slide 13: Effective Shade
Daily direct solar radiation blocked from reaching the stream
Function of shade duration and shade quality
ES = 100-53/100 = 47%
12
12
12
12
10
8
8
10
8
8
12
Graphic modified from Boyd & Kasper 2003
8
10
2
4

## Slide 14: Measuring Effective Shade

## Slide 15: Measuring Effective Shade

## Slide 16: Shade Duration

## Slide 17: Primary Shade Fairview Unit 13
120’ horizontal
100’ horizontal
50’ horizontal
35’ horizontal

## Slide 18: Primary Shade Fairview Unit 13

## Slide 19: Primary Shade Fairview Unit 13

## Slide 20: Secondary Shade Fairview Unit 13

## Slide 21: Primary Shade Fairview Unit 1

## Slide 22: Primary Shade Fairview Unit 1

## Slide 23: Secondary Shade Fairview Unit 1

## Slide 24: Near Stream Shade
11 random points / Effective shade 92-97%, average 94%
They can’t read your sign.

## Slide 25: Primary Shade
“At a qualitative level, the primary and secondary shade source layers created by the BLM model could be very useful to land managers… These products can easily be used to identify areas that would benefit from shade management.”

## Slide 26: Effective Shade
“Using pseudo-hemispherical images to estimate shade can be a cost effective method for estimating shade anywhere high density LiDAR data is available by reducing the amount of field work necessary to obtain the numerous field hemispherical photographs typically required to describe a stream reach or parcel of land.”

## Slide 27: LWD Source Areas

## Slide 28: LWD Source Areas

## Slide 29: LWD Source Areas
Effective tree height (Robison & Beschta 1990)
  20cm (8 in) x 1.5m
  20cm x 2m (May & Creswell 2003)
  15cm (6 in) x 3m (Foster et al. 2001)
Buffer steeper slopes
  40 to >200 year old riparian trees in the PNW more likely to fall towards the channel on steep (>40%) hillslopes (Sobota et al. 2006)
DBH | 16 ft. | 32 ft. | 48 ft. | 64 ft. | 80 ft. | 96 ft. | 112 ft. | 128 ft. | 144 ft. | 160 ft. | 176 ft. | 192 ft. | 208 ft.
12 in. | 10 | 9 | 9 | 6 | 5 | - | - | - | - | - | - | - | -
16 in. | 13 | 12 | 11 | 9 | 8 | 5 | - | - | - | - | - | - | -
20 in. | 16 | 15 | 14 | 12 | 11 | 9 | 6 | - | - | - | - | - | -
24 in. | 19 | 18 | 17 | 15 | 14 | 12 | 10 | 7 | - | - | - | - | -
28 in. | 22 | 21 | 19 | 18 | 16 | 13 | 11 | 7 | - | - | - | - | -
32 in. | 24 | 23 | 22 | 20 | 18 | 16 | 14 | 11 | 8 | - | - | - | -
36 in. | 29 | 28 | 27 | 25 | 24 | 23 | 20 | 18 | 15 | 12 | 9 | - | -
40 in. | 32 | 31 | 30 | 28 | 27 | 25 | 23 | 21 | 19 | 16 | 13 | 10 | -
44 in. | 33 | 32 | 31 | 29 | 28 | 26 | 25 | 23 | 21 | 19 | 16 | 13 | 10
48 in. | 37 | 36 | 34 | 33 | 31 | 29 | 27 | 25 | 23 | 21 | 18 | 15 | 11
Data is based on log taper and board foot tables for Douglas-fir on the Coos Bay District. |  |  |  |  |  |  |  |  |  |  |  |  | 
Bole Diameter in Inches at 16-Foot Intervals Up an Average Tree in each DBH Class.

## Slide 30: LWD Source Areas

## Slide 31: Fairview Unit 13
9/2009
9/2013
Thinning 2/2013 – 2/2014 / 125 tpa to 56 tpa / 23 points, average 104’ horizontal

## Slide 32: Fairview Unit 13

## Slide 33: DOGAMI Landslide Agreement
“I don’t want to look at LiDAR anymore. There are too many landslides. I’m going back to the 10m DEM.”

## Slide 34: Beam Path Maintenance

## Slide 35: Wetlands – North Spit

## Slide 36: Wetlands – North Spit

## Slide 37: Wetlands – Dean Creek EVA

## Slide 38
Courtesy of Craig Cornu, South Slough National Estuarine Research Reserve
Subsidence
Dikes reduce tidal flooding and sediment deposition
Drying leads to soil oxidation, decomposition, and consolidation
Grazing and haying reduce organic material
Livestock and machinery compact soils

## Slide 39: Wetlands – Dean Creek EVA
TPI 30m + Hillshade (bare earth)

## Slide 40: Wetlands – Dean Creek EVA

## Slide 41: Hinsdale Garden

## Slide 42: Questions?

## Slide 43: Stream Profiles