## Slide 1
Policy implications from a recent study on Biscuit Fire effects (first)
Study findings as justification for these policy implications (second)
Policy implications: What should be considered in future NEPA documents covering post-wildfire management and fire-hazard abatement activities? Based on what we learned
Limits of inference to study findings: broad given previous absence of evidence of this quality, but here limited to mixed severity regimes

## Slide 2
We need to elevate our concern over the potential losses of soil productive potential resulting from intense wildfire for the following reasons:
To meet the intent of MUSY to “maintain or enhance productivity of the land.”
Potential losses in the forests future capacity to sequester carbon—this means subtrationality not additionality in C credit markets.
Policy implications
Potential losses in capacity to produce biomass energy or wood products to replace fossil-fuel based building and other products.
Potential losses in jobs and the long-term economic foundation for forest-dependent communities.
Potential losses in acres capable of producing late-successional habitat, especially given losses from the fire.
A.
1.
2.
3.
4.
5.

## Slide 3
Consider major changes in post-fire mitigation strategies:
Policy implications
Given huge losses of soil N and C, consider planting or seeding N2-fixing plants in intensely burned areas (BAER).
1.
Consider fertilizing seedlings of trees critical to reconstructing forest structure.
2.
Reduce the excessive focus on erosion control (especially as predicted by WEPP model)
3.
Value native invasives and sprouters to retain remaining nutrients and soil structure.
4.
Consider salvage logging (like in Biscuit) if it can pay for above mitigation efforts.
5.
B.

## Slide 4
Consider major changes in pre-fire mitigation strategies.
Policy implications
Mid-story hardwoods dampened fire and reduced mortality of dominant conifers—consider leaving them when thinning.
2.
C.
1.
Without fuel reduction, thinning can lead to higher mortality than in untreated mature stands (80 to 100 years).
3.
Large woody debris added to canopy mortality (although less than fine fuels)—consider reducing woody debris targets.
Find ways to pay for hazard reduction including flexibility in eastside screens, and especially fire-killed trees.
Improve fire attack strategies, including early response, burnout preparation, and ridgetop roads and trails.
Consider more than just fuels when reducing hazards.
4.

## Slide 5
Elevating our concern over the potential losses of soil productivity?
Considering major changes in post-fire mitigation strategies?
Considering major changes in pre-fire mitigation strategies?
What’s the science behind:
A.
B.
C.

## Slide 6
Long-Term Ecosystem Productivity
LTEP Biscuit Fire study

## Slide 7: Introduction
Brookings
Grant’s Pass
California
The Biscuit Fire
2002
The long-term ecosystem productivity program experiment near Gold Beach, OR, on the western flank of the Biscuit fire
Snowcamp Lookout
Unburned area
Biscuit Fire area
Fairview Mountain block
Sugarloaf burn study block
Pistol River block
Meadow Creek burn study block
Panther Lake block
Various LTEP treatments

## Slide 8: Intro 3
Snowcamp Lookout
Panther Lake block
Pioneer-lo
Control
DF-lo
DF-hi
Late-lo
Late-hi
Pioneer-hi
Douglas-fir,
hi-wood
Douglas-fir,
lo-wood
Late- succession,
hi-wood
Late- succession,
lo-wood
Pioneer,
hi-wood
Control (not shown)
Pioneer,
lo-wood
Aerial view of the Panther Lake block in 1998 air photo.
Background
Biscuit Fire area
Unburned area

## Slide 9: Intro 4
Control, no action
Conditions before the fire in 2002
Thinned, underburned
Similar, 110-yr-old stands in 1995 before treatment
Thin, underplant leave +/- woody debris
Leave untouched
Experimental treatments applied in 1996:
Background: Eight burned LTEP treatments offer evidence on vegetation-fire interactions:
Clearcut, plant Doug-fir +/- woody debris
Pioneers, lo-wood
Douglas-fir, hi-wood
Clearcut, plant pioneers, +/- woody debris
Underburn in 2001
Thinned, hi-wood
Douglas-fir, lo-wood
Pioneers, hi-wood
Thinned, lo-wood

## Slide 10: A1 photos IL3
1998
1993
2002
2004
Thinned, hi-wood treatment

## Slide 11: A2 photos
2002
1993
1998
Douglas-fir, hi-wood
2004

## Slide 12: Initial Results
Data
“Theory”
Interpreting fire effects on ecosystems can be misleading without before and after data, and without unburned controls

## Slide 13: Hypothesis A
Because thinning reduces fuels, it also reduces fire movement and severity.”
we can assess how the fire traveled through these four thinned and unthinned stand types
Four LTEP treatments (two were replicated) offer evidence on thinning-fire interactions:
Underburn in 2001
Late, lo wood
Control, no-action
Because we know the conditions before the 2002 Biscuit Fire,
Late, underburned
Stands were similar in 1995 before the LTEP treatments
Thin, underplant +/- woody debris
Leave untouched
Experimental LTEP treatments applied in 1996:
A.
Late-succession, +/- woody debris
Late, hi-wood
Late-succession, underburned in 2001

## Slide 14: A1 evidence
Expected (theory)
Actual (data)
Control, no-action
Highest mortality
Medium mortality
Low mortality
Late-succession, underburned
Lowest mortality
Late-succession, hi-wood
Late-succession, lo-wood
LTEP treatment

## Slide 15
Expected (theory)
Actual (data)
Control, no-action
(2 stands)
Highest mortality
Medium mortality
Theory fails
Low mortality
Thinned, underburned
Lowest mortality
Theory works
Thinned, hi-wood
Thinned, lo-wood
(2 stands)
LTEP treatment
92% mortality
64% survival
36% mortality
70% mortality
100% mortality
30%
survival
Theory fails
Theory fails

## Slide 16
Why did controls burn less intensely than thinned stands as predicted by fire models?
Controls had low fine woody fuels (30 and 9 Mg/ha) relative to 28 and 37 for thinned-lo, and 44 Mg/ha for thinned-hi stands.
Controls retained mid-story hardwoods (madrone, tanoak, chinkapin) and they did not act as fuel ladder as predicted, and rather appeared to dampen the fire (much lower char heights).
Still much to be learned about fire behavior.
Evidence to consider:

## Slide 17: B1 evidence
Control, no-action
Thinned, hi-wood
Thinned, lo-wood
Thinned, under-burned
Douglas-fir, hi-wood
Pioneers, hi-wood
Sustained above 700 °C
Moment above 700 °C
Below 700 °C
KEY
Panther block
Fairview block
Burn study block B
The temperature of the Biscuit Fire
Fire temperatures across the 6-acre measurement plots of the LTEP experiments as measured by the extent that aluminum tags melted that were attached to rebar marking our 25-m grid system.
Result: Temperatures observed were enough to volatilize N, S, and possibly P and K. Further studies are needed to examine these potential losses.
Douglas-fir, hi-wood
Pioneers, lo-wood
Not burned
Not burned
Not burned
Not burned

## Slide 18
Before Biscuit
After Biscuit
Issues with measuring soil change
Methods matter
Post-fire surface rocks suggest fixed-depth methods can be highly inaccurate
Background changes suggest that pre-fire condition (1992) does not reflect condition just before the fire (2002)

## Slide 19
Effects of intense wildfire: direct evidence for substantial losses from mineral-soil horizons
20
10
Murphy 12
Dyrness 7
Baird 16
6 hotly burned LTEP stands
Soil-C loss (Mg ha-1)
Literature range
5
15
25
23
6 hotly burned LTEP stands
Literature range
Carbon
O-horizon (40% of 23)
Mineral (60% of 23)
0
Soil-N loss (kg ha-1)
200
400
600
800
Murphy 490
Grier 855
Dyrness -8
690
Nitrogen
O-horizon 297 (43% of 690)
Mineral 393 (57% of 690)
1600
1400
1200
1000
Baird 1700
In the case of intense fire, losses of soil C are far from minimal as widely assumed

## Slide 20
Effects of intense wildfire: indirect evidence for losses in long-term site productivity and C sequestration
Short-term negatives
Increased
Total C and N
SOM and mineral soil
Infiltration
Water-holding capacity
Cation-exchange capacity
Energy supply for microbes
Reduced
Bulk density
Soil-C loss (Mg ha-1)
Carbon
20
10
5
15
25
23
O-horizon
Mineral
Soil-N loss (kg ha-1)
Nitrogen
0
200
400
600
800
690
O-horizon
Mineral
1000
0
Profile C = 74
Lost soil C = 31%
Profile N = 3000
Lost soil N = 23%

## Slide 21
Effects of intense wildfire: indirect evidence for losses in long-term site productivity and C sequestration
Soil-C loss (Mg ha-1)
Carbon
20
10
5
15
25
23
O-horizon
Mineral
Soil-N loss (kg ha-1)
Nitrogen
0
200
400
600
800
690
O-horizon
Mineral
1000
0
Profile C = 74
Lost C = 31%
Profile N = 3000
Lost N = 23%
Does a 23 Mg/ha loss equal a 20% decline in productive capacity?
Thinned
Short-term negatives
Increased
Total C and N
SOM and mineral soil
Infiltration
Water-holding capacity
Cation-exchange capacity
Energy supply for microbes
Reduced
Bulk density
Homann et al. 2004

## Slide 22
Effects of intense wildfire: indirect evidence for losses in long-term site productivity and C sequestration
Soil-C loss (Mg ha-1)
Carbon
20
10
5
15
25
23
O-horizon
Mineral
Soil-N loss (kg ha-1)
Nitrogen
0
200
400
600
800
690
O-horizon
Mineral
1000
0
Short-term positives
Nutrient availability?
Cations in ash
Mineral surfaces stripped of organic coatings
Increased
Reduced
Pathogens
Competition (for sprouting plants)
Short-term negatives
Increased
Total C and N
SOM and mineral soil
Infiltration
Water-holding capacity
Cation-exchange capacity
Energy supply for microbes
Reduced
Bulk density

## Slide 23
Effects of intense wildfire: indirect evidence for losses in long-term site productivity and C sequestration
Soil-C loss (Mg ha-1)
Carbon
20
10
5
15
25
23
O-horizon
Mineral
Soil-N loss (kg ha-1)
Nitrogen
0
200
400
600
800
690
O-horizon
Mineral
1000
0
Other nutrient losses at temps observed (>780 °C):
N: 200 °C
P and K: 774 °C
Ca and Mg: 1000 °C
Longer-term probabilities
Losses of mineral-soil C that were recalcitrant to decomposition (product of previous microbial attacks), will take many decades to rebuild.
Losses of soil N will take >300 years to be replaced without N2-fixers?
Nonetheless, resiliency processes are poorly understood—and we need to follow actual responses.
If collective plant growth (trees and shrubs) is reduced, CO2 uptake, return of C and N to soil, and weathering will slow?

## Slide 24
Overview on sampling methods
Soil samples
1992
2003
7-ha LTEP treatment “stand”
1.5-ha “measurement plot”
25-m gridpoint
23 LTEP stands,
12-16 samples per stand,
4 horizons to 30 cm depth,
1992 and 2003:
Total of ~2500 layer samples

## Slide 25
60
Rock (>4 mm) concentration (% total inorganic matter)
0
20
40
0
20
40
60
80
10
5
0
15
20
25
Sampled depth mid-point (cm)
1992
2003
Huge rock gains near surface after fire
No detectable background changes
Hotly burned stands
Unburned stands
burned
Unburned

## Slide 26
Effects of intense wildfire: common methods for assessing soil change need revisiting
Fixed-depth
subsurface layer
Comparable
subsurface layer
Post-fire comparable-layers approach
Pre-fire soil
Post-fire fixed-depth approach
Comparable
surface layer
Fixed-depth
surface layer
The fixed-depth surface layer underestimates fire-induced losses because it ignores particle losses and post-fire measurement is exaggerated by starting and ending at a lower elevation (with lower C & N).
A
Loss of surface fines—both organic and inorganic—leaves a layer of surface rocks, a decrease in volume, and a drop in surface elevation.
A
Original surface
Post-fire surface
B
B
Original bottom
Post-fire bottom
Comparable-layers method accounts for loss of volume and surface fines by using rock and fine-inorganic mass as references.
Missing volume and fine soil

## Slide 27: B4 photos
Erosion pins
Microtopography plots
Erosion boxes

## Slide 28: B10 evidence
Slope (%)
Dumptruck loads per 15 acres
0
40
80
0
10
20
30
40
R2=0.3
Burned
Unburned
Large water-driven soil movement was observed in erosion boxes on steeper, burned slopes.
Little accumulation downslope at stand scale (see photo, at left, of the stream at the base of a 30-acre hotly burned area just above a road).
Erosion measured as changes in erosion boxes in 2nd year after fire

## Slide 29
Oregon
Nevada
California
The Biscuit Fire

## Slide 30
0
20
40
60
80
100
120
Before
After
Carbon (Mg/ha)
Intact logs
Decayed logs
Fine fuels
O-horizon
Mineral soil
Down 38%
Down 100%
Down 89%
Down 100%
Down 22%
Ecosystem C budgets
Results:
Losses of soil C (23 Mg/ha) were about the same as losses from fine and coarse woody fuel C (22 Mg/ha)
Combustion was nearly complete for decayed logs, fine fuels, and the O horizon.
Intact (less decayed) woody debris C was 38% combusted while mineral soil C was 22% combusted.
Which sources of combustion killed the trees is an unanswered question.
Slight evidence of more mortality in hi-wood treatments.

## Slide 31
0
20
40
60
80
100
120
Before
After
Carbon (Mg/ha)
Intact logs
Decayed logs
Fine fuels
O-horizon
Mineral soil
Down 38%
Down 100%
Down 89%
Down 100%
Down 22%
0
100
200
300
Before
After
Carbon (Mg/ha)
Live trees
Snags
Down 100%
Ecosystem C budgets
New snags become the biggest C pool.
Lots of implications that are poorly understood.